## Slide 1
SMART SECURITY
DOOR LOCK SYSTEM
Project Documentation · 3-Phase Development
Phase 1: Tinkercad Prototype | Phase 2: Wokwi Simulation | Phase 3: Real Implementation

## Slide 2
Project Overview
A progressive 3-phase development of an Arduino-based smart door lock, starting from a basic prototype and evolving into a fully-featured real-life security system.
01
Basic Prototype
Tinkercad
Simple button-controlled lock with servo motor, LED indicators, and auto-lock timer. Built on Arduino UNO.
02
Full Simulation
Wokwi + Arduino Mega
Advanced system with RFID, 4×4 keypad, LCD display, EEPROM, multi-user roles, lockout & admin menu.
03
Real Implementation
Arduino UNO
Physical build with RFID RC522, 3×4 keypad, LCD 16×2, buzzer, servo & full feature parity on live hardware.

## Slide 3
Phase 1
Basic Prototype — Tinkercad (Arduino UNO)
Concept validation with a minimal component set

## Slide 4
Phase 1 — Circuit Diagram (Tinkercad)
🟦 Arduino UNO
Main microcontroller
🔵 Push Button
Pin 2 — Lock trigger
🔴 Red LED
Pin 4 — Locked state
🟢 Green LED
Pin 3 — Unlocked state
⚙️ Servo Motor
Pin 9 — Door bolt (0°/90°)

## Slide 5
Phase 1 — How It Works
1
System Start
Arduino initialises — servo moves to 0° (LOCKED), Red LED turns ON.
2
Button Press Detected
A LOW→HIGH transition on Pin 2 triggers the unlock sequence.
3
Door Unlocked
Servo rotates to 90°, Red LED OFF, Green LED ON. Serial log: 'Door unlocked!'
4
Auto-Lock (3 s)
After 3 000 ms the system automatically re-locks — servo to 0°, Red LED ON.
5
Manual Re-lock
A second button press while unlocked immediately re-locks the door.

## Slide 6
Phase 1 — Code Highlights
// Key constants & objects
const int BUTTON_PIN = 2; const int GREEN_LED = 3;
const int RED_LED = 4; const int SERVO_PIN = 9;
Servo doorLock; bool isLocked = true;
const int AUTO_LOCK_DELAY = 3000; // 3 seconds
// Unlock → wait → auto-lock sequence
if (isLocked) {
isLocked = false; updateLockState();
delay(AUTO_LOCK_DELAY); // door stays open 3 s
isLocked = true; updateLockState(); // auto-lock
}
// updateLockState() — drives LEDs + servo
doorLock.write(isLocked ? 0 : 90); // 0°=LOCKED 90°=UNLOCKED

## Slide 7
Phase 2
Full Simulation — Wokwi (Arduino Mega)
RFID · PIN Keypad · LCD · EEPROM · Multi-user · Admin Menu

## Slide 8
Phase 2 — Simulation Circuit (Wokwi)
Components
▸ Arduino Mega 2560
▸ MFRC522 RFID Reader (SPI)
▸ 4×4 Matrix Keypad
▸ LCD 16×2 (I2C, 0x27)
▸ Servo Motor (Pin 6)
▸ Buzzer (Pin 7)
▸ Red LED (Pin 5) + Green LED (Pin 4)

## Slide 9
Phase 2 — Key Features
🪪
RFID Auth
Scan registered cards for instant access by UID matching.
🔢
PIN Entry
4–8 digit PIN via 4×4 keypad; # to confirm, * to clear.
👥
4 User Roles
Admin · User (×2) · Guest — each with unique PIN & card.
🔒
Lockout System
6 failed attempts triggers 30 s lockout with alarm sound.
🛡️
Admin Override
Admin PIN unlocks the system even during lockout.
💾
EEPROM Persist
PINs, UIDs, lockout state saved across power cycles.
🚨
Panic Code
Entering '911' activates an emergency alarm sequence.
🔇
Silent Mode
Admin can mute all buzzer sounds via the menu.

## Slide 10
Phase 2 — System State Machine
SYS_IDLE
SYS_LOCKED
ADMIN_LOGIN
ADMIN_MENU
ROLE_SELECT
USER_EDIT
CHANGE_PIN
6 fails
* Admin PIN
1 PIN
State transitions respond to keypad input, RFID scans, and timeout events.

## Slide 11
Phase 3
Real-Life Implementation — Arduino UNO
Physical hardware build with full feature parity

## Slide 12
Phase 3 — Real-Life Build
Hardware Pin Map
Arduino UNO
Main controller
RFID RC522
SS=10, RST=9 (SPI)
3×4 Keypad
Rows: 2,3,8,A0 | Cols: A1,A2,A3
LCD 16×2 (I2C)
Address 0x27
Servo Motor
Pin 6 — 90°=locked, 0°=open
Buzzer
Pin 7 — tones & alarm
Red LED
Pin 5 — denied / locked
Green LED
Pin 4 — granted / open

## Slide 13
Phase 3 — UNO Adaptations vs Mega
Feature | Phase 2 (Mega) | Phase 3 (UNO) | Notes
Keypad | 4×4 (16 keys) | 3×4 (12 keys) | A–D keys removed; * and # retained
Pin-out | Dedicated ports (22–29) | Analog pins A0–A3 used | UNO pin shortage workaround
Servo motion | Instant write() | Smooth ramp loop | ±2° steps for realistic door motion
LCD icons | No custom chars | Lock / Unlock icons | lcd.createChar() byte arrays
Card menu | Not present | Full 2-option card menu | Set card, remove card per user
User select | Direct key to user | Role → User two-step | Extra state SYS_USER_SELECT
Flash strings | Normal strings | F() macro used | Saves SRAM on 2 KB UNO

## Slide 14
Phase 3 — Code Highlights
// Smooth servo motion — unique to Phase 3 (UNO)
void openDoor() {
doorServo.attach(SERVO_PIN);
for (int p = LOCK_POS; p >= UNLOCK_POS; p -= 2) {
doorServo.write(p); delay(10); // gradual unlock
} delay(200); doorServo.detach();
}
// F() macro — saves precious 2 KB SRAM on UNO
show(F("SCAN CARD"), F("OR ENTER PIN"));
// RFID card override during lockout (new in Phase 3)
if (uidBelongsToAdmin(uid, size)) {
clearLockout(); show(F("RFID OVERRIDE"), F("LOCK CLEARED"));
}

## Slide 15
Phase Comparison
Feature | Phase 1 | Phase 2 | Phase 3
Microcontroller | Arduino UNO | Arduino Mega | Arduino UNO
Auth Method | Push Button | RFID + PIN | RFID + PIN
Display | Serial Monitor | LCD 16×2 (I2C) | LCD 16×2 (I2C)
Keypad | None | 4×4 Matrix | 3×4 Matrix
Users | Single | 4 (Admin/User/Guest) | 4 (Admin/User/Guest)
EEPROM | No | Yes | Yes
Lockout | No | Yes (30 s) | Yes (30 s)
Admin Menu | No | Yes | Yes
Panic Code | No | Yes (911) | Yes (911)
Card Assign | No | No | Yes (via menu)
Smooth Servo | No | No | Yes (ramp)
Platform | Tinkercad | Wokwi | Real Hardware

## Slide 16
Project Conclusions
✅ Phase 1 validated the core lock/unlock mechanic with minimal components.
✅ Phase 2 proved the full security architecture in a risk-free virtual environment.
✅ Phase 3 demonstrated real-world feasibility on limited Arduino UNO hardware.
✅ EEPROM persistence ensures settings survive power loss.
✅ Role-based access, lockout, admin override & panic mode provide layered security.
🔮 Future work: WiFi/BLE remote unlock, camera integration, mobile app control.
Smart Security Door Lock System · 3-Phase Arduino Project